## Slide 1
Secure Processor Design
by
Shayan Taheri
University of Central Florida
Orlando, Florida
Fall 2015

## Slide 2
Overview
Introduction
Related Work
Questions
2
Notes: These are the topics that are covered in this presentation.
2

## Slide 3
Introduction
Security → A new processor design parameter → Why?
  Protection of trusted code and data
  Integrity verification of computations
  Prevention of unauthorized access to system and network
3
Notes: 3

## Slide 4
Introduction …
Security and Processor
  Processor for Security → Provision of security from processor
    Example: Cryptographic Processors
  Security of Processor → Provision of security for processor
    Why? → Possible attacks and threats for processors
    Example: Malicious modifications, bugs, virus, and etc.
4
Notes: 1) The digital methods are not reliable any more.
2) Solution: Using the analog signaling behaviors of the devices or in other words concentrating on the Physical Domain.
3) In fact, there are unique variations in the analog signals of the devices that can be used for identification and monitoring purposes.
4) These unique features are due to hardware and manufacturing inconsistencies.
4

## Slide 5
Introduction …
Countermeasures for Attacks
  Physical Analysis (After Fabrication)
    Destructive → Reverse-engineering
    Nondestructive → Functional Verification and Side-Channel Analysis
  Design Analysis (Before Fabrication)
    Information Flow Tracking
    Functional Verification
5
Notes: 1) Fingerprint: A repetitive and always present signal.
5

## Slide 6
Introduction …
Functional Verification
  Formal Verification
  Model Checking → VLSI Testing and Verification
  Run-Time Verification
6
Trojan Insertion inside Processor

## Slide 7
Related Work
Security Checkers: Detecting Processor Malicious Inclusions at Run-time
  A run-time verification technique
  Property Specification Language → A standard assertion language
  Inclusion of synthesizable assertion functions into hardware design
  Experiment → The Plasma CPU → A 32-bit MIPS architecture
    Memory write verification
    Delay → Additional one clock cycle for every write operation
    Area Overhead → + 0.1%
7
Notes: 1) Steady-State Portion: It has sufficient amount of information.
7

## Slide 8
Related Work …
Architectural Support for Copy and Tamper Resistant Software
  A secure processor design technique → XOM Architecture
  Targeting processor interactions with memory
  Implementation of cryptographic algorithms on these interactions
8
Hash Value
Tag
Encrypted Data
Message Format from Processor
Tag && Data && Interrupt Counter
Hash Function
Notes: 1) Matched filter: An optimal detector that is sensitive enough to perceive the small variations in a device’s signal.
2) Adaptive Thresholding Strategy: It is used for calculating and updating the threshold range for the upcoming data.
8

## Slide 9
Related Work …
FANCI: Functional Analysis for Nearly-unused Circuit Identification
  A model checking technique
  Goal: Finding possible infected sites in a digital IC
  How? → The input wire(s) effect of each component on its output wire
    Having a vector of “Control Values” for each output wire
  Outcome → Suspicious wires → Nearly stuck-at fault wires
  My Implementation using C++ Language  1574 Number of Lines!
9

## Slide 10
A
A | B | C
0 | 0 | 0
0 | 1 | 0
Input “A” Fixed at 0
A | B | C
1 | 0 | 0
1 | 1 | 1
Input “A” Fixed at 1
Control Value =
Number of Conflictions
Number of Rows in Each State
Confliction
B
C
0.5
0.5
Method Name | Run Time (Minute : Second) | (%)
Average | 5:30 | 3.7225
Median | 5:24 | 3.9590
Method Name | Run Time (Minute : Second) | 
Average | 5:30 | 3.7225
Median | 5:24 | 3.9590
Infected NoC Router
Related Work …

## Slide 11
Related Work …
Physical Layer Identification (PLI)
  A side-channel analysis technique
  Targeting processor interactions with networking devices
  Using the first layer of the OSI model for device identification
  PLI Methodology
    Identify and acquire a device's signal (i.e. Fingerprint)
    Extract a set of meaningful features from the signal
    Compare the test feature set with the reference feature set
    Determination of the device identity
11
Notes: 1) Fingerprint: A repetitive and always present signal.
11

## Slide 12
12
Related Work …
Device Tampering by Temperature Variation

## Slide 13
Questions
13